## Slide 1: A subkeV energy threshold spherical gazeous detector for light Dark Matter identification
August 14th 2013
Quy Nhon, “Window on the Universe”
G Gerbier IRFU Saclay
+ I Giomataris, J Derre, P Magnier, A Dastgheibi, D. Jourde, M Gros, E Bougamont, XF Navick, T Papaevangelou, J Galan, G Tsiledakis IRFU
P Loaiza, T Zampieri LSM
Principles of detector
Results of calibrations at low energy
Preliminary results at low energy/RA
Prospects : physics / development

## Slide 2: Spherical Proportional Counters
Drift region
Ampl region
E≈V/r2*rs
for rc>> rs
rs
rc
Sphere cavity + spherical sensor + HT
=> Low threshold (low C), does not depend on size
Fiducial volume selection by pulse risetime
Flexible (P, gaz)
Works in sealed mode
Large volume => 10’s kg possible
2 LEP cavity 130 cm Ø tested
Digitisation at 2 MHz + soft trigger

## Slide 3: Spherical Proportional Counters
Drift region
Ampl region
Point like
deposition
Track
Sphere cavity + spherical sensor + HT
=> Low threshold (low C), does not depend on size
Fiducial volume selection by pulse risetime
Flexible (P, gaz)
Works in sealed mode
Large volume => 10’s kg possible
2 LEP cavity 130 cm Ø tested
Digitisation at 2 MHz + soft trigger
1 low activity 60 cm Ø in operation @ LSM

## Slide 4: Run with Ar/CH4 + 3g 3He @ 200 mb SPC 130cm Ø @ LSM
Rise time (s)
Amplitude
 210Po
5.3 MeV
n capt on 3He
764 keV
222Rn 218Po 214Po
If point like energy deposition, rise time depends only on radius of interaction (diffusion)
If track, rise time depends on orientation of track, ie on difference of drift times
NB: no start
=> risetime records place and/or history of energy deposition
Uncovoluted
alpha
de/dx

## Slide 5: Run with Ar/CH4 + 3g 3He @ 200 mb SPC 130cm Ø @ LSM
Rise time (s)
Amplitude
 210Po
5.3 MeV
n capt on 3He
764 keV
 210Po
5.3 MeV
from 210Pb
@ Cu surface
Range = 15 cm
n capt on 3He
=> p + T
222Rn 218Po 214Po
Unwanted Radon daughter deposit on surface
1
2
3
fast neutron expected here
Rate 400 capt/d
« Volume » alpha

## Slide 6: Going to low energy : calibration with 37Ar source for volume response
37Ar, EC, 35 days lifetime, Ka 2.6 keV and Lb 260 ev
Source made by n,a from Calcium powder irradiated with fast neutrons
=> Calibration show homogenous volume response
260 eV
2.6 keV

## Slide 7: Calibration with UV flash pulsed lamp for single electron response
Delta time (UV-sphere pulse)
Look for pulse in 200-260 ms window
About 1 in 10 => single electron response
Trigger @ 10 ADU
Trigger efficiency for single electron = 54 %
NB : single electron in Ar gaz w ≈ 30 eV
=> Threshold = 20 eV
1 electron
16 ADU 30 eV
ms
Single electron
distribution
250 mb, Ar+2%CH4
HV = 3100 V
14 mm sensor
Pulse shape

## Slide 8: Light dark matter search : low activity 60 cm Ø prototype @ LSM in PE/Pb shield
In test since september 2012
Test of sensors from 14 mm to 6 mm
Reduction of RA contaminants
Commisionning runs with Argon (but 39Ar intrinsic radioactivity)
=> Run with Neon+2%CH4 @ 2 bars
=> 200 g sensitive mass, 48 h run
eV
eV
Preliminary
Data

## Slide 9: Light dark matter search : low activity 60 cm Ø prototype @ LSM
eV
eV
Preliminary
In operation since september 2012
Test of sensors from 14 mm to 6 mm
Reduction of RA contaminants
Commisionning runs with Argon (but 39Ar intrinsic radioactivity)
=> Run with Neon+2%CH4 @ 2 bars
=> 200 g sensitive mass, 48 h run

## Slide 10: Light dark matter search : low activity 60 cm Ø prototype @ LSM
eV
eV
Signal from 2.2 GeV WIMP, with s = 1.1 10-37 cm2
assuming QF =0.3
Preliminary
In operation since september 2012
Test of sensors from 14 mm to 6 mm
Reduction of RA contaminants
Commisionning runs with Argon (but 39Ar intrinsic radioactivity)
=> Run with Neon+2%CH4 @ 2 bars
=> 200 g sensitive mass, 48 h run
100 eV

## Slide 11: Light dark matter search : low activity 60 cm Ø prototype @ LSM
eV
eV
300
/kg.kev.d
More probable : background !
Many knobs :
  Pressure
  Gaz change (He)
  HV
In operation since september 2012
Test of sensors from 14 mm to 6 mm
Reduction of RA contaminants
Commisionning runs with Argon (but 39Ar intrinsic radioactivity)
=> Run with Neon+2%CH4 @ 2 bars
=> 200 g sensitive mass, 48 h run
Background flat rate

## Slide 12: Sensitivity curves for light WIMP’s

## Slide 13: Sensitivity curves for light WIMP’s
GeV/c2
10-37
10-39
10-38
10-40
5
Actual sensitivity 100 evts/kg.keV.d @ 0.8 keV NR
Projected sensitivity for 1 evt/kg.keV.d @ 0.3 keV NR
Ne
Preliminary
Ne
NB : still very high surface contamination by Po210/Pb210 by factor 50

## Slide 14: Additional discrimination identification through single/multiple energy deposition
Recorded pulse
RC
Uncovoluted from RC shaping
Simulation by J Galan

## Slide 15: Test run with Ne (2bars)+He (2bars) 8h He gives longer drift times => better identification of multiples
Volume selection events ≈ 40 % eff
Red : after single energy deposition selection
Energy eV
rt
ms
=> Need simulation of pulse shapes of electrons and neutrons
Need calibration with Ar37 and fast neutron for accurate efficicencies
Need study of rejection power vs gaz mix
…
Energy eV

## Slide 16: Other applications
Axion Like Particle detection : (decays in 2 photons inside sphere volume) motivation : solar corona temperature problem L. Di Lella, K. Zioutas, Astropart. Phys. 19 (2003) 145(J Galan)
Thermal and fast neutron detection : interest : containment of products of capture eg He3, other gaz studied
Network of 4m Ø spheres for SuperNovae neutrino detection through coherent scattering (about 10 evts for 10 kpc SN @10 atm Ar)
Measurement of neutrino coherent scattering at reactor …

## Slide 17: Measuring coherent neutrino scattering at nuclear reactor within reach
20 ev/keV.kg.d
80 ev/keV.kg.d
Evis >30 eV
30 eV
Assumptions :
120 days exposures OFF and ON
Rate back = 500 evts/kg.d.keV
ROI = 30-250 eV
=>Nback= 500*37*120*0.22= 500 000 evts
=>Nsig = 24 000 evts
=> S/N = 1/20 , Ns = 24
eV
Simulation of expected spectrum from nuclear reactor, on Ar, with quenching factor and instrumental response to single electron
Normalisation to experimental reactor 70 MW
Sphere of 2 m diam, 5 bars

## Slide 18
CEA-IRFU/Saclay (GG,IG),LSM (F Piquemal),
Aristotle University of Tessaloniki (I Savvidis), University of Ioannina (I Vergados), NCSR DemoKritos (G Fanourakis), Hellenic Open University (S Tzamaria)
University of Tsinghua Beijing (C Tao), Shanghai Jiao Tong University (K Ni),
IHEP-Beijing (Z Wang, C Yang)
University of Saragoza (I Irastorza), Livermore (JR Armendariz)
A proto collaboration
New Experiments With Spheres
Neutrino Experiments With Spheres
New Experiments for Wimps with Spheres
Tessaloniki 2012
Projects under study
4 m Ø underwater 2000 m @ Pylos @ few 100s bars for SN
2 m Ø underground low activity for DM and ALP search shielded in water tank
Perform n coherent scaterring expt
Develop neutron spectrometer
Develop sensors + scint light detection
+ Great tool for training to particle detection !

## Slide 19
CEA-IRFU/Saclay (GG,IG),LSM (F Piquemal),
Aristotle University of Tessaloniki (I Savvidis), University of Ioannina (I Vergados), NCSR DemoKritos (G Fanourakis), Hellenic Open University (S Tzamaria)
University of Tsinghua Beijing (C Tao), Shanghai Jiao Tong University (K Ni),
IHEP-Beijing (Z Wang, C Yang)
University of Saragoza (I Irastorza), Livermore (JR Armendariz)
A proto collaboration
New Experiments With Spheres
Neutrino Experiments With Spheres
New Experiments for Wimps with Spheres
Tessaloniki 2012
Projects under study
4 m Ø underwater 2000 m @ Pylos @ few 100s bars for SN
2 m Ø underground low activity for DM and ALP search shielded in water tank
Perform n coherent scaterring expt
Develop neutron spectrometer
Develop sensors + scint light detection
Great tool for learning training !

## Slide 20: Conclusions/outlook
First studies show that spherical gaz detector :
  can indeed reach single ionisation electron sensitivity @ P>1 atm
  has background rejection capabilities and redondancies to identify signal
  is well adapted for low mass WIMP search 0.1 to 5 GeV
  has potential for neutrino coherent scattering detection & other LE rare processes
Developments to improve performances of current prototype
  Decrease high radioactive contamination : surface
  Improve pulse shape analysis : calibration, templates…
  Perform calibration with neutron/Ar37
  Perform quenching factor measurements in keV region (D Santos installation at Grenoble)
Going to larger volume/pressure requires
  Decoupling of amplification from drift : new ideas about sensors currently tested
  + R&D on scintillation measurement, …
  … lot to develop and discover

## Slide 21: Quenching factor (He) measurements by D Santos down to 1.5 keV
Big difference below 5 keV between calc and exp
Measurement : 23 % vs prediction : 45 % ??
Difference attributed to UV light scintillation production

## Slide 22: Système d’Acquisition
HV CAEN SY127; 8KV;2µA
Ampli de charge
Sensibilité = 180 mV/pC
Bruit ≤ 500 ē
Carte ADC «CALI» développée à l’IRFU
FÉchantillonnage =1-5 MHz
Gain : 1, 2 et 4
Bruit ≤ 250 ē
© CANBERRA
Rj45
ADC
Amp
Filtre
Capacité de liaison
Un seul câble pour la H.T et la détection du signal
Mac

## Slide 23
CAEN SY127; 8KV;2µA
Ampli de charge
Sensibilité = 180 mV/pC
Bruit ≤ 500 ē
Carte ADC «CALI» développée à l’IRFU
FÉchantillonnage =1-5 MHz
Gain : 1, 2 et 4
Bruit ≤ 250 ē
Programme d’acquisition :
« SAMBA » => trigger, record
(Développé par M.GROS,
IRFU/SEDI pour Edelweiss)
Signaux typiques
Système d’Acquisition
Rj45
ADC
AOP
Filtre
Capacité de liason
260 eV
40 eV