## Slide 1
The CALorimetric Electron Telescope (CALET):
A High Energy Cosmic-ray Observatory
on the International Space Station
Shoji Torii
for the CALET Collaboration
Waseda University &
Japan Aerospace Exploration Agency (JAXA)
CALET
Very High Energy Universe in the Universe
Quy Nhon, Vietnam August 4-9, 2014

## Slide 2
CALET International Collaboration
CALET is a
Recognized
Experiment
Waseda University
ASI
NASA

## Slide 3
CALorimetric Electron Telescope overview
Calorimeter
The CALorimetric Electron Telescope, CALET, project is a Japan-led international mission for the International Space Station, ISS,
in collaboration with Italy and the United States.
JEM-EF Port #9
The CALET payload will be launched by the Japanese carrier, H-II Transfer Vehicle 5 (HTV5) and robotically attached to the port #9 of the Japanese Experiment Module – Exposed Facility (JEM-EF) on the International Space Station.
Weight: 650 kg
Mission Life: 5 years
Launch Target: by March, 2015
(Fiscal Year 2014)
Gamma - Ray Burst Monitor

## Slide 4
CALET
Approach to ISS
Pickup of CALET
H2 Transfer Vehicle（HTV)
Launching by
H2B Rocket
Separation from H2B
Launching Procedure of CALET
HTV
HTV
ISS
HTV Exposed Palette
Attach to JEM-EF
CALET

## Slide 5
Science Objectives | Observation Targets
Nearby Cosmic-ray Sources | Electron spectrum into trans-TeV region
Dark Matter | Signatures in electron/gamma energy spectra in the several GeV – 10 TeV range
Cosmic-ray Origin and Acceleration | p-Fe energy spectra up to 1015 eV and trans-iron elements (Z=26-40) at a few GeV
Cosmic–ray Propagation in the Galaxy | B/C ratio above TeV /nucleon
Solar Physics | Electron flux below 10 GeV
Gamma-ray Transients | Gamma-rays and X-rays in the 7 keV - 20 MeV range
CALET Science Goals
The CALET mission will address many of the outstanding questions of
High Energy Astrophysics, such as the origin of cosmic rays,
the mechanism of CR acceleration and galactic propagation,
the existence of dark matter and nearby CR sources.

## Slide 6: CALET Payload Overview
ASC (Advanced Stellar Compass)
CAL/CHD
CAL/IMC
CAL/TASC
CGBM/SGM
MDC (Mission Data Controller)
FRGF (Flight Releasable Grapple Fixture)
CGBM/HXM
GPSR
(GPS Receiver)
HV Box
(by ASI)
・ Mass: 650 kg
・ Size (JEM-EF Standard Payload) : L1850 × W800× H1000 mm
・ Power: 650 W（nominal）
・ Data rate： medium 600 kbps, low 35 kbps
CGBM
HXM x2
LaBr3(Ce)
SGM x1
BGO
7keV-1MeV
0.1-20MeV
CHD
IMC
TASC
CHD-FEC
IMC-FEC
TASC-FEC
CHD-FEC
IMC-FEC
TASC-FEC
CAL (CHD/IMC/TASC)

## Slide 7
CALET instrument characteristics
1 TeV electron shower
45 cm
 | CHD (Charge Detector) | IMC (Imaging Calorimeter) | TASC (Total Absorption Calorimeter)
Function | Charge Measurement (Z=1-40) | Arrival Direction, Particle ID | Energy Measurement, Particle ID
Sensor (+ Absorber) | Plastic Scintillator : 14 × 1 layer (x,y) Unit Size: 32mm x 10mm x 450mm | SciFi : 448 x 8 layers (x,y) = 7168 Unit size: 1mm2 x 448 mm Total thickness of Tungsten: 3 X0 | PWO log: 16 x 6 layers (x,y)= 192 Unit size: 19mm x 20mm x 326mm Total Thickness of PWO: 27 X0
Readout | PMT+CSA | 64 -anode PMT(HPK) + ASIC | APD/PD+CSA PMT+CSA ( for Trigger)@top layer
Field of view: ~ 45 degrees (from the zenith)
Geometrical Factor: 0.12 m2sr (for electrons)
Unique features of CALET
Thick, fully active calorimeter:
Allows measurements well into
the TeV energy region with
excellent energy resolution
Fine imaging upper calorimeter:
Accurately identify the starting
point of electromagnetic showers.
Detailed shower characterization:
Lateral and longitudinal
development of showers enables
electrons and abundant protons
to be powerfully separated.

## Slide 8
Gamma-ray 10 GeV
Electron 1 TeV
Proton 10 TeV
Proton rejection power of 105 can be achieved with IMC and TASC shower imaging capability.
Charge of incident particle is determined to σZ=0.15-0.3 with the CHD.
CALET/CAL Shower Imaging Capability (Simulation)
In Detector Space

## Slide 9: CALET Expected Performance by Simulations
Angular resolution for gamma ray (10GeV-1TeV):
s = 0.2-0.3 deg
Proton rejection power at 1TeV ≈105 with 95% efficiency for electrons
Geometrical factor for electrons:
~1200 cm2sr
Energy resolution for electrons (>10GeV) :
s/m = ~2%
Charge resolution:
σZ = 0.15e(@B) – 0.30e(@Fe)
Preliminary
electrons
protons
Preliminary
electrons
protons
CHD
Experiment
@CERN-SPS

## Slide 10
Electron & Positron Origins and Production Spectrum
Evolution of the Universe
Dark Matter Origin
水素、
ヘリウム
４
%
暗黒エネルギー
暗黒エネルギー
暗黒物質
暗黒物質
重元素
0.03%
ニュートリノ
0.3%
星
0.
５
%
暗黒物質
25%
暗黒エネルギー
暗黒エネルギー
暗黒物質
暗黒物質
重元素
0.03%
ニュートリノ
0.3%
星
0.
５
%
暗黒物質
25%
暗黒エネルギー
70%
宇宙の質量構成比
宇宙の質量構成比
水素、
ヘリウム
４
%
水素、
ヘリウム
４
%
暗黒エネルギー
暗黒エネルギー
暗黒物質
暗黒物質
重元素
0.03%
ニュートリノ
0.3%
星
0.
５
%
暗黒物質
25%
暗黒エネルギー
暗黒エネルギー
暗黒物質
暗黒物質
Heavy Element
0.03%
Neutrino
0.3%
Star
0.
５
%
Dark Matter
2３%
Dark Energy
7３%
Constitutes of
the Universe
Hydrogen、
Helium
４
%
(ⅰ) Monoenergetic: Direct Production of e+e- pair
（ⅱ）Uniform：Production via Intermediate Particles
（ⅲ）Double Peak： Production by Dipole Distribution
via Intermediate Particles
Mχ
Annihilation of Dark Matter（WIMP)
χχ→e+,e-
Power Law Distribution
with a Cutoff
Shock Wave Acceleration in SNR
Acceleration in PWN
Astrophysical Origin
dN/dE  E-2exp(-E/Ec)
Log(E)
Log(dN/dE)
Ec
↑
e++e-
etc.
Typical Distribution Depending
on the Mass and Type of DM

## Slide 11
e± Propagation in the Galaxy

## Slide 12
    T (age) = 2.5 ×105 × (1 TeV/E) yr
    R (distance) = 600 × (1 TeV/E)1/2 pc
> 1 TeV Electron Source:
Age < a few105 years
very young comparing
to ~107 year at low energies
Distance < 1 kpc
nearby source
Source (SNR) Candidates :
Vela Cygnus Loop Monogem
Unobserved Sources?
Nearby Sources of Electrons in TeV region
(F0: E3 x Flux at 3TeV)
Contribution to 3 TeV Electrons
from Nearby Source Candidates

## Slide 13
CALET Main Target: Identification of Electron Sources
Expected flux
for 5 year mission
Expected Anisotropy
from Vela SNR
~10% @1TeV
> 10 GeV | ~ 2.7 x 107
>100 GeV | ~ 2.0 x 105
>1000 GeV | ~ 1.0 x 103
Some nearby sources, e.g. Vela SNR, might have unique signatures
in the electron energy spectrum in the TeV region (Kobayashi et al. ApJ 2004)
Identification of the unique signature from nearby SRNs,
such as Vela in the electron spectrum by CALET

## Slide 14
Cosmic Ray Positron Excess

## Slide 15
Dark Matter Search by e++e- Observation – LSP decay-
Expected e++e- spectrum by Lightest Super Symmetry Particle (LSP)
after 5-year CALET measurement, which is consistent with present data of positron excess and e++e- spectrum

## Slide 16: Pulsar Energy Spectrum: Fine Structure
Yin+ 13
Kawanaka, KI & Nojiri 10
Multiple pulsars make fine structure
Large sample(cosmic) variance
at high energy
Poisson
dispersion
Best Fit of e++e- -energy spectrum for ATNF pulsars
from [Malyshev et al. PRD 2009 ] to AMS02+Fermi/LAT
(black line) and of a Single Pulsar spectrum (green line) .
By using 1000 CALET 5-yr samples (grey dots):
− The fine structure (black line) is observable by
CALET thanks to the high energy resolution
− With more than 5σ if the Single Pulsar case is
assumed (red lines).

## Slide 17
Detection of High Energy Gamma-rays
Simulation of point source observations in one year
Energy Range | 4 GeV-10 TeV
Effective Area | 600 cm2 (10GeV)
Field-of-View | 2 sr
Geometrical Factor | 1100 cm2sr
Energy Resolution | 3% (10 GeV)
Angular Resolution | 0.35 ° （10GeV)
Pointing Accuracy | 6′
Point Source Sensitivity | 8 x 10-9 cm-2s-1
Observation Period (planned) | 2014-2019 (5 years)
Performance for Gamma-ray Detection
Simulation of Galactic Diffuse Radiation
~25,000 photons are expected per one year
*) ~7,000 photons from extragalactic
γ-background (EGB) each year
Geminga: ~150 photons above 5 GeV
Crab: ~ 100 photons above 5 GeV
Vela: ~ 300 photons above 5 GeV
Energy Spectrum
Position
Position

## Slide 18
Monochromatic gamma-ray signals from WIMP dark matter annihilation would provide a distinctive signature of dark matter, if detected. Since gamma-ray line signatures are expected in the sub-TeV to TeV region, due to annihilation or decay of dark matter particles, CALET, with an excellent energy resolution of 2- 3 % above 100 GeV, is a suitable instrument to detect these signatures .
Detection Capability of Gamma-ray Lines from Dark Matter
Gamma-ray excess in
the Galactic Center?
A 130 GeV line?
Simulated gamma-ray line spectrum for 2yr from neutralino annihilation toward the Galactic center
with m=820GeV, a Moore halo profile, and BF=5

## Slide 19
Energy reach in 5 years:
Proton spectrum to ≈ 900 TeV
He spectrum to ≈ 400 TeV/n
P and He Observation
CALET expected in 5 y (red points)
p and He spectra at TeV are harder than the low-energy spectra and have different slopes in the multi TeV region (CREAM)
Hardening in the p and He at 200 GV observed by PAMELA
Hint of concavity due to CR interactions with the shock?
Cutoff in the p spectrum (proton knee) ?
Different types of sources or acceleration mechanisms?
However AMS-02 did not observe any break or spectral features

## Slide 20
Intermediate Nuclei to Fe Observation
CALET expected in 5 y (red points)
CALET energy reach in 5 yr
~20 TeV/n : C, O, Ne, Mg, Si
~10 TeV/n : Fe
CALET energy resolution for nuclei 20÷30% independent on energy
All primary heavy nuclei spectra well fitted to single power-laws with similar spectral index (CREAM, TRACER)
However hint of a hardening from a combined fit to all nuclei spectra (CREAM)
 Possible features (concave spectrum) or spectral breaks?

## Slide 21
B/C ratio measurements by CALET
E –δ
δ＝0.3
δ=0.6
At high energy (> 10 GeV/n) the B/C ratio measures the energy dependence of the
escape path-length，~E-δ， of CRs from the Galaxy
Data below 100 GeV/n indicate δ~0.6. At high energy the ratio is expected to flatten out (otherwise CR anisotropy should be larger than that observed)
Balloon experiments CREAM and TRACER measured the B/C ratio up to ~1 TeV/n
But: - large statistical error (limited exposure)
- large systematic errors due to corrections for B produced by interaction of
of heavier nuclei with atmosphere
CALET can measure in 5 years the B/C ratio up to 5-6 TeV/n.
CALET measurements in orbit
free from atmospheric production of boron
CALET can also measure the sub-Fe over Fe abundance ratio.

## Slide 22
Ultra heavy nuclei abundances provide information on CR site and acceleration mechanism
CHD resolution is ~constant above 600 MeV/n Charge ID from saturated dE/dx
No need to measure energy  No passage through TASC  Large acceptance ~0.4 m2sr
The energy threshold cut is based on the vertical cutoff rigidities seen in orbit
CALET should collect in 5 years 2-4 times the statistics of TIGER, w/o corrections for residual atmosphere overburden
Geomagnetic Latitude
CALET (expected) vs. TIGER data
Ultra Heavy Nuclei

## Slide 23
CHD
Plastic Scintillator
+ Light Guide
Plastic Scintillator Layer
IMC
TASC
SciFi Layer
Structure of IMC
Random Vibration Test
PWO + APD/PD
Structure of TASC
Random Vibration Test
©JAXA
Hardware Development: Structure and Thermal Model (STM)

## Slide 24
CERN Beam Test using the STM
Charge Detector: CHD
Imaging Calorimeter: IMC
Total Absorption Calorimeter: TASC
Schematic Side View of the Beam Test Model
The Beam Test Model at CERN SPS H8 Beam Line
ΔE-Ebeam
Electron shower
transition curve
in TASC
Angular resolution
for electrons
Beam Test Results

## Slide 25: General Alerts of Transients
MSFC/NASA
JAXA
Tsukuba SC
CALET Ground System in UOA
Data Processing
in
Waseda CALET Operations Center (WCOC)
GCN, ATel,
Web
Alerts
・GCN:
Gamma-ray Coordinates Network
・ATel:
Astronomer’s Telegram
Counterpart search
Further follow up observations in longer EM wavebands
CALET on ISS
LIGO-Virgo MOU
CGBM data
・TH: Timing Histogram
・PH: Pulse height Histogram
・GRB triggered data
TDRSS
DRTS

## Slide 26
Conclusions
CALET is a space-based calorimeter designed to perform cosmic ray measurement with high energy resolution, mainly aimed at the electron component
Its main instrument is a deep (27 X0), homogeneous, segmented PWO calorimeter, which provides both an excellent energy resolution and a high e/p rejection power
CALET will investigate the spectrum of many cosmic ray species in a broad energy range, providing valuable information for indirect DM search, and study acceleration and propagation mechanisms
Development of the CALET flight hardware is now well underway
The CALET project has been approved for flight by HTV-5 to the Japanese Experiment Module (Kibo) , to be launched by March 2015
The expected mission is 5 years
-> electron exposure = 220 m2 sr days

## Slide 27
Comparison of Space Experiment Performance for e++e-
Payload (Launching Date) | Energy Region (GeV) | Energy Resolution | e/p separation | Instruments* | Exposure in 5 years** （m２ sr day) | Total Weight (kg)
PAMELA (2006) | 1-700 | 5 % @200 GeV | 105 | Magnet Spectrometer (0.43T) + Sampling Calorimeter (Si＋W: 16 X0) +TOF+ Neutron Detector | ~ 4 | 470
FERMI/LAT (2008) | 20-1,000 | 5-20 % (20-1000 GeV) | 103-104 (20-1000GeV) Increase with Energy | ACD Detector +Tracking Calorimeter (Si＋W: 1.5X0) +CsI Cal. (8.6X0) | 1500@TeV | 7.000
AMS-02 (2011) | 1-2,000 (~800) | ～10 ％ ＠100 GeV | 104 -105 | Magnet Spectrometer (0.15T) + Sampling Calorimeter (SciFi + Pb: 17Xo) +TOF+TRD+RICH | 55@2TeV (170@800GeV) | 7,000
CALET (2014) | 1-20,000 | ~2 % (>10 GeV) | ~105 Mostly Energy Independent | Imaging Calorimeter (W+SciFi: 3 Xo) + Total Absorption Cal. (PWO : 27 Xo) ＋Charge Detector (SCN) | 220 | 650
DAMPE* (China：2015?) | 5-10,000 | ~1.5 % | ~105 | Silicon Tracker +Total Absorption Cal. (BGO: ~31 X0) +ACD Detector +Neutron Detector | 900 | 1,500
GAMMA-400* (Russia：2017?) | 1-sevral 10,000 | ~1 % (>100GeV) | ~4x105 | Imaging Calorimeter (2X0) + Main Calorimeter- calocube (25 X0) | 730(vertical) x10 (all) | 1,700
*) Estimated from Presentations

## Slide 29
Model Dependence of Energy Spectrum and Nearby Source Effect
Ec: Cutoff Energy ΔT: Acceleration Period D: Diffusion Constant at 1 TeV (∝E0.6)
Ec=∞、 ΔT=0 yr, Do=2x1029 cm2/s
Do=5 x 1029 cm2/s
Ec= 20 TeV
Ec=20 TeV、 ΔT=104 yr
Kobayashi et al. ApJ (2004)
uniform source distribution

## Slide 30
Gamma Line: Differences to HESS
● Very stringent limit but localized search.
● Max. 1.58 deg distance from GC only
● Limit depends on halo profile, used Einasto profile with general factor for
subhalo distribution
● Could have missed nearby subhalos
(extragalactic search also because data from point source observation)
● Wide (2 sr) field of view
● Search in outer regions of galactic halo
– less dependent on halo profile, extragalactic background only
● Certain to see nearby subhalos providing large boost factor
● Up to larger energy than Fermi-LAT

## Slide 31: Energetics
U(proton)
~1eV/cm3
← Supernova
remnants
U(electron)
~10-2eV/cm3
U(positron)
~10-3eV/cm3
~ 0.1% of p
Even less @TeV
0903.1987
e-2.7

## Slide 34
Expected Allowed Region for LKP
Tested several Dark Matter candidate particles scanning the mass from
200 GeV to 4 TeV for ability to explain positron excess only by emission
from annihilation – given a sufficiently high boost factor
If fit without pulsar term to AMS-02 and Fermi/LAT data gives χ2 <95%CL: allowed model => LKP allowed for mass > 500 GeV => Range of boost factor with χ2 <95% CL: allowed region (blue region)
Assuming m(LKP)=1000 GeV the allowed region can be significantly reduced by including CALET data (red region)
Assuming the Pulsar Case, a much smaller contribution from Dark Matter would already be excluded (red line)

## Slide 35
Characteristics of HXM and SGM in CGBM
HXM
SGM
BGO
LaBr3

## Slide 36
Parameters | CAL | CGBM
Energy range | 1 GeV - 10 TeV (GRB trigger) | HXM: 7 keV - 1 MeV (goal 3 keV - 3 MeV) SGM: 100 keV - 20 MeV (goal 30 keV - 30 MeV)
Energy resolution | 3% (10 GeV) | HXM: ~3% (662 keV) SGM: ~15% (662 keV)
Effective area | ~600 cm2 (10 GeV) | 68 cm2 (2 HXMs), 82 cm2 (SGM)
Angular resolution | 2.5° (1 GeV) 0.35° (10 GeV) | -
Field of view | ~45° (~2 sr) | ~3 sr (HXM), ~4π sr (SGM)
Dead time | 2 ms | 40 µs
Time resolution | 62.5 µs | GRB trigger: 62.5 µs (event-by-event data) Normal mode: 125 ms with 8 ch, 4 s with 512 ch (histogram data)
Broad energy range (from few keV X-rays to GeV-TeV gamma-rays):
long-duration GRBs, short-duration GRBs, X-ray flashes and GeV GRBs.
Sensitivity of CGBM: ~10-8 ergs cm-2 s-1 (1-1000 keV) for 50 s long bursts.
CALET GRB performance
Notes: N: (Yamaoka) The deadtime for the CAL is now 5.8 ms, not 2 ms. Finally it will be > 2 ms, still to confirmed.

## Slide 37
CALET Science Data Flow
Collaboration with
LIGO/Virgo