## Slide 1: Status and prospects for MW-class accelerators - Intensity frontier proton accelerators -
Tadashi Koseki
J-PARC center, KEK&JAEA
NuFact2016
Quy Nhon, Vietnam, August 23, 2016

## Slide 2
- Status and future plan of intensity frontier accelerators
Multi-MW accelerator facilities
Summary

## Slide 3
Status and future plan of intensity frontier accelerators

## Slide 4: Hadron accelerators in the world
J. Wei / Y. Yamazaki
1 MW

## Slide 5: MW-class proton accelerators operating as front-runners
Spallation Neutron Source, ORNL
1-GeV AR, 1.4 MW
Main Injector, FNAL
120-GeV Synchrotron, 700 kW
J-PARC, KEK&JAEA
3-GeV RCS, 1 MW / 30-GeV MR , 750 kW
HIPA, PSI
590 MeV/u cyclotron, 1.4 MW

## Slide 6: SNS Accelerator Complex
Front-End:
Produce a 1-msec long, chopped, H- beam
1 GeV LINAC
Accumulator Ring: Compress 1 msec long pulse to 700 nsec
2.5 MeV
LINAC
Front-End
Accumulator Ring
RTBT
HEBT
Injection
Extraction
RF
Collimators
945 ns
1 ms macropulse
Current
mini-pulse
Chopper system makes gaps
Current
1ms
Liquid Hg Target
1000 MeV
M. Plum
The first hadron accelerator facility which adopts SRF linac technology extensively.

## Slide 7: SNS beam power vs time
SNS reached 1 MW user operation within 5 years from the beginning in 2006.
Demonstrated full design beam power of 1.4 MW for >24 hours for neutron scattering experiments in June 2014.
Failures on target were stronger limit on operational beam power than the accelerator in the last 4 years.
Courtesy of M. Plum
1.4 MW
1.0 MW

## Slide 8: PSI proton accelerator facility
Courtesy of M. Seidel
The first accelerator facility which realized 1-MW stable user operation in the world.
A separated sector cyclotron
A flattop cavity, 3rd harmonic resonator, decreases energy spread and increases acceptance. The beam current can be increased from 1 mA to 2.4 mA.

## Slide 9: History of peak current in the PSI accelerator
license operation with 2.2mA given: 1.3MW
4 new Cu Resonators in Ring complete
aperture limitation removed; new ECR source; 50Hz ripple problem solved: 1.4MW
plasma problems
M. Seidel
Accelerator upgrade towards 3mA/1.8 MW are now studied; injector upgrade, new flattop cavity, new collimators behind muon production target.

## Slide 10: Fermilab Accelerator Complex (enabled by PIP-I)
H- linac : Accelerates H- to 400 MeV
Booster : 400 MeV  8 GeV at 15 Hz since June 2015 , h=84
Beam delivery to RR/Low energy neutrino experiments
Recycler Ring: a permanent magnet accumulator ring in the MI tunnel, h=588 ( 7*84)
6+6 booster batches are injected to RR using slip-stacking
Beam delivery to the MI and the Muon campus simultaneously.
Main Injector: 8 GeV 120 GeV at 1.33 s cycle time
Beam delivery to High energy neutrino experiments /SY120
Simultaneous operations of NOvA and SY120 (slow extraction beam)
0.5 sec.
Courtesy of S. Nagaitsev

## Slide 11: Beam power for NOvA
M. Convery at ICHEP2016
RR
MI
Booster
Revolution time of RR
Slip-stacking with 6+6 batches
0.8 s

## Slide 12: Ramp up to > 700 kW
On going upgrade for > 700 kW user operation:
Add new collimators in the RR
Add two more cavities in booster for reliability and eliminating losses
New injection scheme of the booster
etc.
~one minute demonstration

## Slide 13: PIP-II
Performance Parameter | PIP-II | 
Linac Beam Energy | 800 | MeV
Linac Beam Current | 2 | mA
Linac Beam Pulse Length | 0.5 | msec
Linac Pulse Repetition Rate | 20 | Hz
Linac Beam Power to Booster | 13 | kW
Linac Beam Power Capability (@>10% Duty Factor) | ~200 | kW
Mu2e Upgrade Potential (800 MeV) | >100 | kW
Booster Protons per Pulse | 6.4×1012 | 
Booster Pulse Repetition Rate | 20 | Hz
Booster Beam Power @ 8 GeV | 120 | kW
Beam Power to 8 GeV Program (max) | 80 | kW
Main Injector Protons per Pulse | 7.5×1013 | 
Main Injector Cycle Time @ 120 GeV | 1.2 | sec
LBNF Beam Power @ 120 GeV* | 1.2 | MW
LBNF Upgrade Potential @ 60-120 GeV | >2 | MW
Goal: Provide >1 MW at the time of LBNF startup (~2023)
800 MeV superconducting pulsed linac + enhancements to existing complex
Courtesy of S. Nagaitsev

## Slide 14: J-PARC
400-MeV H- linac
3-GeV RCS with 25 Hz
30-GeV MR with cycle time of 2.48/5.52 sec
RCS is proton driver for neutron/muon production in MLF and booster for the MR.
MR has a lattice of imaginary transition g and two extraction modes (FX and SX).

## Slide 15
Earthquake
300 kW
Hg-target
replacement
Radioactive material leak incident at
Hadron Facility
as of 30th of June 2016
1 MW eq. (~8.4e13 ppp) demonstration
～1 month interruption
due to the fire in MLF
Beam Power History at MLF
Interruption due to troubles of Hg-target
500 kW
Beam Power [kW]
Accumulated Beam Power [MWh]

## Slide 16
Achieved beam power:
Fast extraction ~ 425 kW (2.2x1014 ppp) for users , 440 kW for demonstration.
Slow extraction ~42 kW (4.9 x1013 ppp) for users , 50 kW for demonstration.
Beam power history of MR
Beam stop due to the earthquake
Beam stop due to the radioactive material leak incident in HEF

## Slide 17: Mid-term plan of MR
JFY | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 |  |  |  | HD target (80kW) |  |  | HD target (>100 kW)
FX power [kW] SX power [kW] | 390 42 | 425-450 42-50 | 450-500 50 | 700 50-70 | 800 80 | 900 80 | 1060 ~100
Cycle time of main magnet PS New magnet PS | 2.48 s |  |  | 1.3 s | 1.3 s | 1.25 s | 
High gradient rf system 2nd harmonic rf system |  |  |  |  |  |  | 
Ring collimators | Add.collimators (2 kW) |  | Add.colli. (3.5kW) |  |  |  | 
Injection system FX system |  |  |  |  |  |  | 
SX collimator / Local shields |  |  |  |  |  |  | 
Ti ducts and SX devices with Ti chamber |  |  | ESS |  |  |  | 
Mass production
installation/test
Manufacture, installation/test
Kicker PS improvement, Septa manufacture /test
Kicker PS improvement, FX septa manufacture /test
Local shields
FX：The high repetition rate scheme is adopted to achieve the design beam intensity, 750 kW. Rep. rate will be increased from ~ 0.4 Hz to ~1 Hz by replacing magnet PS’s, RF cavities and some injection and extraction devices.
SX： The beam power of the MR will be gradually increased toward 100 kW watching the residual activity. In the HEF, the primary target will be replaced new ones which have more cooling capability in 2018 and 2021.
Installation
New PS buildings
COMET / high-p physics run

## Slide 18
Magnet PS upgrade
2.48  1.3 s cycle
1.25 s cycle
1.20 s cycle
1.16 s cycle
Air-cooled 2nd RF
RF anode power supply upgrade
10th RF system
JFY
Beam power projection of MR fast extraction
Notes: This picture shows expected power.
Horizontaｌ is JFY and vertical is beam power.
Now we are here.
Here , we have magnet PS upgrade and after that cycle time is gradually shortened.
And we plan to upgrade RF anode power supply here. And we reach 1.3 MW in 2023, if budget is approved as the plan.

## Slide 19
g-2/EDM (0.1ppm/10-21 e cm)
at MUSE in the MLF
Ultra-Cold Muon Beam
with muon linac RFQ,IH,disk-loaded
- Ultra-Precision Magnetic Field
  3T, 1 ppm
COMET(I <10-14; II < 10-16)
Search for muon to electron conversion
Adopted staging approach
Phase-I: 10-14 (already funded)
Phase-II: 10-16
32 m SC solenoid magnet
Beam extinction < 10-9
8 GeV, 3.2 kW(Phase-I) and 56 kW(Phase-II)
Phase I
Phase II

## Slide 20: Reliability and residual activation for high intensity proton facilities
S. Cousineau, “High Power Proton Facilities: Operational Experience, Challenges, and the Future”, Proc. IPAC2015
Synchrotron and rings have much higher residual activation. But they should be improved by better understanding beam loss mechanism and reducing uncontrolled beam losses in spite of beam intensity increasing.

## Slide 21: Challenges in the high beam intensity accelerators
Challenges on beam dynamics
Eliminating beam loss due to collective effects
- Space charge effects,
Beam instabilities – due to coupling impedance, electron cloud effects
Beam halo – to understanding the mechanism of halo formation is important for high power operation.
Gamma transition jump in synchrotron
Challenges on hardware
Cutting edge technologies should be developed for accelerator systems.
- Charge exchange injection
Beam collimators
Extraction devices and methods (specially for slow extraction)
Precise beam monitors with wide dynamic range
Superconducting rf technology with high performance and cost effective
High power targetry / Beam window

## Slide 22: Space charge issues on high power beam operation
Space charge tune shift at J-PARC MR :
Intensity of synchrotrons/accumulator rings are limited by space-charge effect at injection energy. In order to avoid beam loss due to betatron resonances in the presence of space charge tune shift ;
- Correction of resonances
- Increase bunching factor
- Rise the injection energy
- Increase physical aperture…
Number of protons: 2.5e13 ppb
(380 kW @2.48s cycle)

## Slide 23: ASTA/IOTA project at Fermilab
ASTA/IOTA project is aiming at breakthrough research to increase beam power (x 3-5 times) in future proton rings.
IOTA (Integrable Optics Test Accelerator)
Can operate with either electron or proton
Large aperture
Significant flexibility of the lattice
Precise control of the optics quality and stability
Set up for very high intensity operation with proton
R. Zwaska in HINT2015 workshop
Slide from R. Zwaska in HINT2015

## Slide 24: Target improvement
SNS Target failures
  Five out of the last eleven targets have failed at weld joints
Leak detector fluid “bubbling” through weld failure on the target
2014
J-PARC also had unscheduled beam shutdown due to troubles on mercury targets two times in 500 kW user operation in 2015. Causes of the both cases are weld failures.
  New targets are designed to improve / eliminate weld joints for higher reliability.
M. Plum
High Power Targetry is one of key technologies for the future high power facilities.
R&D’s on a material behavior regarding a thermal shock and radiation damage in target should be conducted tenaciously.

## Slide 25
Multi-MW accelerator facilities

## Slide 26: 2nd target station and beam power upgrade
 | Present | Upgrade
Number of particles | 1.5e14 ppp | 2.4e14 ppp
Beam energy | 1 GeV | 1.3 GeV
Beam power | 1.4 MW | 2.8 MW
Linac 60 Hz: FTS 50 Hz, 2-2.3 MW
STS 10 Hz, 0.47 MW
RFQ peak current : 33  46 mA
Chopping fraction : 0.7  0.82
Courtesy of M. Plum

## Slide 27: ESS(European Spallation Source)
Courtesy of H. Danared
Construction started in 2014.
First beam on target at 572 MeV in June 2019
Start user operation in 2023
ESSnuSB project  N. Vassilopoulos in the WG3 session

## Slide 28: ESS accelerator
Beam dynamics rule of thumb:
The zero current phase advance per period in all the planes must be less than 90 deg
The phase advance per meter (average phase advance) variation should be smooth and continuous
The tune depression, ksc/k0 , must stay above 0.4 in all the planes during acceleration
Courtesy of H. Danared

## Slide 29: Neutron production target
Neutron intensity/pulse for ESS and other operating facility
Courtesy of H. Danared
Features and requirements
Rotating target wheel
36 tungsten sectors
5 MW heat removal
Helium gas cooling
High brightness modurators
Confinement and shielding

## Slide 30: Accelerators for ADS
MYRRHA (Belgium)
Proton linac 600 MeV, 2.4 MW
- Demonstrate the ADS concept at pre- industrial scale
Demonstrate transmutation
Multipurpose and flexible irradiation facility
C-ADS (China)
Proton linac 1.5 GeV, 15 MW
Two alternatives developed:
→ test operation and technical selection in 2016
- Phase I : R&D facility
Phase II : Experimental facility
      ~10 MW (~2032)
Phase III: Demo facility
IHEP
IMP
W. Pan and J. Dai,”ADS based on linear accelerator”, Review of accelerator Science and technology, Vlo. 8 (2015) World Scientific.

## Slide 31: PIP-III
From “High Power Proton Beams for Particle Physics ” Sergei Nagaitsev,
11th ICFA seminar on Future Perspective in High Energy Physics

## Slide 32
Beta & Dispersion for 1-superperiod
bx,y (m)
hx,y (m)
H & V
s (m)
J-PARC: The 8-GeV booster ring
(x,x’)
(y,y’)
@ 3GeV
@ 8GeV
e>125.5p ~0.04%
e>54p ~0.06%
Phase plot @ inj.(3GeV) & extr.(8GeV)
8 GeV injection in the MR using new septa&kickers
RCS : 1.6 MW
MR > 2.6 MW
RCS : 2 MW
MR > 3.2 MW
8-GeV BR
INJ+COLL
RF CAVs
RF CAVs
EXT
Injection energy 3 GeV
Extraction energy 8 GeV
Circumference 696.666 m
Superperiodicity 4
Transition gamma ~15 GeV
Collimator Aperture 126π.mm.mrad
Physical Aperture 189 π.mm.mrad

## Slide 33: The proton driver in the KEKB Tunnel
To Kamioka
1.2 GeV
3.3 GeV
6.2 GeV
9 GeV
Three 650 MHz
rebunchers
Three 1.3 GHz
rebunchers
Three 1.3 GHz
rebunchers
For the acceleration in the 2nd to 4th straight section, the ILC cavity is adopted.
- Outline of acceleration :
  1.2 GeV in 1st straight.
  3.3 GeV in 2nd straight.
  2.9 GeV in 3rd and 4th straight. 3.3 + 2.9 x 2 = 9.0 GeV
- Peak current : 100 mA (pulse)
- Beam duty : 1 %
- Beam power : 9 GeV x 0.1 A x 1 % = 9 MW
Layout of front-end and the 1st straight section
Details were given by G. T. Park in WG3 session

## Slide 34
Thanks all the contributors;
H. Danared, Mats Lindroos (ESS), S. Nagaitsev, R. Zwaska (FNAL), M. Seidel (PSI), M. Plum (SNS), M. Ikegami (FRIB), S. Igarashi, H. Harada, H. Hotchi, T. Maruta, F. Maekawa, G. T. Park, Y. Sato, H. Takada (J-PARC).
During past decade, accelerator facilities for neutron/muon generation, PSI and SNS, advanced the frontier of beam intensity and realized 1 MW with high operational availabilities.
High energy accelerators for neutrino experiments were also frontier of beam intensity. They will reach beam power > 1 MW by the beginning of 2020s if the budgets are approved as planed.
Multi-MW facilities like ESS, accelerators for ADS, PIP-III and J-PARC 8 GeV booster / 9 GeV proton driver are studied / constructed.
Deep understanding of beam dynamics and R&Ds of cutting edge technologies should be pursued continuously and also in international collaboration.
Summary

## Slide 35: Backup

## Slide 36: New power supply for high repetition rate operation
Large scale PS for bending magnets and quad. magnets in arc setions
Two large converters and large capacitance for energy recovery, symmetric power module circuit
磁石
C−bank
C-bank
トランス
小電力
大電力（全磁気エネルギー）
Filter
Magnet
DC-DC
Convert-or
AC-DC
Convert-or
Transformer
Small power
Large power (full mag. power)
Results of prototype PS
The 1st quadrupole PS will be transferred to J-PARC and tested in the 2016 summer shutdown period.
Construction of the three buildings will be finished in August of 2017.
D1-3: existing buildings
D4-6: Newly constructed buildings
Budget for three buildings of the magnet PS’s and for starting mass production of the PS’s have been approved by the government in JFY2016.
Y. Kurimoto

## Slide 37
Feasibility of the RCS
RCS intensity | Loss | Loss power at 25 Hz
1.0 MW | ~0.3% | 400 W
1.1 MW | ~0.3% | 440W
1.2 MW | ~0.3% | 480 W
1.3 MW | ~0.3% | 520 W
1.4 MW | ~0.3% | 560 W
1.6 MW | ~0.5% | 1067 W
1.8 MW | ~0.7% | 1680 W
2.0 MW | ~1.5% | 4000 W
Loss (%)
Injection beam parameters:
Energy : 400 MeV
Peak current : 50 mA~100 mA
Pulse length: 0.5 ms
Chopper-beam on duty : 0.53
Beam intensity
RCS collimator limit ~4 kW
→ RCS has a feasibility to operate 2 MW
Linac 100 mA/0.5 ms (50 mA/1.0 ms) operation is required.
R&D of ion source / long pulse operation of linac
The rf system should be replaced to compensate a heavy beam loading.
The collimator capability should be upgraded to get a margin for the beam loss.
Activation downstream of the charge exchange foils should be reduced.
….

## Slide 38
Time (ms)
Number of particles / pulse (x1013)
Demonstration of 1 MW-eq. beam in RCS
8.41 x 1013 :1010 kW-eq.
6.87 x 1013 :825 kW-eq.
4.73 x 1013 :568 kW-eq.
7.86 x 1013 :944 kW-eq.
5.80 x 1013 :696 kW-eq.
Collimator section
First arc section (near the dispersion peak)
Mainly due foil scattering during injection
8.41 x 1013
6.87 x 1013
4.73 x 1013
7.86 x 1013
5.80 x 1013
Time (ms)
BLM signals @ collimator & arc sections
Beam loss < 0.1 % ( < 133 W ) << 4 kW collimator limit
First arc section
ー 1014 kW-eq. : 8.45 x 1013
ー 870 kW-eq. : 7.25 x 1013
ー 731 kW-eq. : 6.09 x 1013
ー 606 kW-eq. : 5.05 x 1013
ー 473 kW-eq. : 3.94 x 1013
We are ready to start 1 MW operation in the RCS.
Collimator section
Time (ms)
H. Hotchi

## Slide 39: Toward the beam intensity > 1MW
Higher rf voltage and more operating margin
Reinforcement of anode power supplies to increase anode current of power amplifier
Additional rf system (# 10)
Air-cooled second harmonic rf system
mitigating space charge effect.
VHF rf system
mitigating space charge effect.
(Suppression of the longitudinal instabilities)
BPM upgrade
more precise and faster measurement.
FX kicker upgrade
Low beam coupling impedance
Beam Power (kW) | 425 (Achieved) | 813 | 1000 | 1326
#ppp(1014) | 2.2 | 2.2 | 2.6 | 3.2
Rep T (s) | 2.48 | 1.3 | 1.3 | 1.16
Measured bunching factor and longitudinal distribution of 3.2x1013 ppb (~1 MW for 1.3 s cycle)
Without 2nd harmonics
With 2nd harmonics

## Slide 40
Decreasing beam loss due to space charge in J-PARC MR
Two bunches,
3-GeV accumulation
Correction of linear coupling resonance by skew quadripoles
2nd harmonic rf voltage
Bunching factor

## Slide 41: High Intensity beam study
Beam loss due to the horizontal instability
D BPM signal
Horizontal
Vertical
Near future tunable knobs to reduce the beam loss:
Injection kicker, BxB feed-back, 2nd harmonic cavity, etc.
- at the new betatron tune (21.239, 21.310) -
High power trial with two bunches
Extracted beam : 3.41e13 ppb
6.82e13 ppp (132 kW eq. ,2 bunches)
 | Bunch number | repetition period (sec) | Beam power (kW) | Beam loss (kW) | Notes
1 | 2 | 2.48 | 132 | 0.42 | measurement
2 | 8 | 2.48 | 529 | 1.7 | estimation
3 | 8 | 1.3 | 1009 | 3.2 | estimation
Total beam loss ~ 420 W
The MR has capability to reach 1MW with the high repetition rate operation.
Details will be given by Y. Sato in WG3 session