## Slide 1: High power beam operation at J-PARC: status and future
Yoichi Sato (KEK / J-PARC)
for J-PARC accelerator group
concerning MR beam commissioning
NuFact16, August 23, 2016

## Slide 2: Outline
Introduction
  J-PARC MR and FX operation
Recent tunings
  Beam loss sources
  instability: chromaticity correction and transverse feedback
  optics correction during acceleration
  resonance corrections
  2nd harmonic rf: larger bf, less sc effect
  New operation point explore
Midterm plan
  High repetition scenario
  For > 1MW
Summary

## Slide 3
Neutrino Beam Line for T2K Experiment (30 GeV)
Materials & Life Science Facility (MLF) (3 GeV)
3 GeV Rapid Cycling Synchrotron (RCS)
Hadron Experimental Hall (HD) (30 GeV)
400 MeV H- Linac
Main Ring Synchrotron (MR)
Japan Proton Accelerator
Research Complex (J-PARC)
Notes: T2K experiment (long base line Nu oscillation experiment)

## Slide 4: Main parameters of MR
Circumference 1567.5 m
Injection energy 3 GeV
Extraction energy 30 GeV
Super-periodicity 3
harmonic 9
Number of bunches 8
Rf frequency 1.67 - 1.72 MHz
Transition  j 31.7 (typical)
Physical Aperture
3-50 BT Collimator 54-65 p.mm.mrad
3-50 BT physical ap. > 120 p.mm.mrad
Ring Collimator 54-70 p.mm.mrad
Ring physical ap. > 81 p.mm.mrad
Three dispersion free straight sections of 116-m long:
- Injection and collimator systems
- Slow extraction（SX)
to Hadron experimental Hall
- RF cavities and Fast extraction(FX) (beam is extracted inside/outside of the ring)
outside: Beam abort line
inside: Neutrino beamline ( intense  beam is send to SK)

## Slide 5: Main parameters of MR
Circumference 1567.5 m
Injection energy 3 GeV
Extraction energy 30 GeV
Super-periodicity 3
harmonic 9
Number of bunches 8
Rf frequency 1.67 - 1.72 MHz
Transition  j 31.7 (typical)
Physical Aperture
3-50 BT Collimator 54-65 p.mm.mrad
3-50 BT physical ap. > 120 p.mm.mrad
Ring Collimator 54-70 p.mm.mrad
Ring physical ap. > 81 p.mm.mrad
TWO OPERATION MODE:
Fast extraction mode (FX) for the neutrino oscillation experiment: 1 turn extraction
Slow extraction mode (SX) for the hadron hall experiments: 2 s extraction.
FX Cycle time 2.48 s
SX Cycle time 5.52 s
Beam power [W]
= Ave. Beam Current [A=C/s] × Beam Energy [eV]
= Number of charged particles [C/pulse]×Number of pulse [pulse/s] × Beam Energy [eV]
More particles, higher repetition  High power

## Slide 6: Typical Operation Status for Fast Extraction
2.15e14 ppp at extraction = 416 kW
(4 batches = 8 bunches)
2.7e13 protons/bunch
*2 bunches at each injection
Injection
Acceleration
Extraction
Recovery
0.13 s
1.4 s
0.95 s
2.48 sec cycle
Smoothing
Smoothing
Beam Intensity with DCCT
Collimator area
Integrated BLM count
Non-collimator area
Monitor sensitivity×8
Address in the whole MR
Time (s)
Time structure
BLM count
Notes: KEYS:
Basics: COD corr., Optics meas. and corr., Injection matching,
Tune flatness at optimal tune, Collimator balance
For Instability: Chromaticity patterned corr., Transverse FB
Resonance corr: Skew Q

## Slide 7: Typical Operation Status for Fast Extraction
MR total beam loss ~600 W < MR collimator capacity 2 kW
3-50BT beam loss ~100 W < 3-50BT collimator capacity 2 kW
2.15e14 ppp at extraction = 416 kW
(4 batches = 8 bunches)
2.7e13 protons/bunch
*2 bunches at each injection
Injection
Acceleration
Extraction
Recovery
0.13 s
1.4 s
0.95 s
2.48 sec cycle
Smoothing
Smoothing
MR total loss ~600 W
(inj. ~170 W + acc. ~420 W) W
Beam Intensity with DCCT
Collimator area
Integrated BLM count
Non-collimator area
Monitor sensitivity×8
Beam loss localized
in collimator area
Address in the whole MR
Time (s)
Time structure
BLM count
Beam losses are well localized in collimator area and low energy time zone
Notes: KEYS:
Basics: COD corr., Optics meas. and corr., Injection matching,
Tune flatness at optimal tune, Collimator balance
For Instability: Chromaticity patterned corr., Transverse FB
Resonance corr: Skew Q

## Slide 8: MR Beam Power History
In the operation of Jan ~ May 2016, the beam power was mostly about 390 kW with 2×1014 protons per pulse. With the same protons per pulse, the designed beam power 750 kW can be achieved after the faster cycling from 2.48 s to 1.3 s.
The user operation of 415~425 kW was successful in May 2016.
The first beam in MR:
May 2008: Injection;
Dec. 2008: acceleration and extraction
The max. delivered beam power
~ 425 kW (2.2x1014 ppp)

## Slide 9: Outline
Introduction
  J-PARC MR and FX operation
Recent tunings
  Beam loss sources
  instability: chromaticity correction and transverse feedback
  optics correction during acceleration
  resonance corrections
  2nd harmonic rf: larger bf, less sc effect
  New operation point explore
Midterm plan
  High repetition scenario
  For > 1MW
Summary

## Slide 10: Beam loss sources and Tuning Items for Fast Extraction
Beam loss sources in MR
Upstream beam quality from RCS:
 In Transverse, to choose optimal conditions with 3-50BT OTR monitor
Physical aperture
 to hold effective aperture with closed orbit correction, optics correction
Emittance growth by Betatron resonances
 To choose optimal operation point considering
- Tune spread by space charge
 to control high bunching factor with higher harmonic RF
- Tune spread by chromaticity
 patterned Chromaticity correction with sextupoles
- Resonance strength
 to enlarge dynamic aperture by
leakage field corrections with Trim-quadrupoles
resonance corrections with Skew-quadrupoles, Trim-Sextupoles
optics meas. & correction not only injection period but acceleration period
Emittance growth by beam instability (impedance from resistive wall)
 transverse feedback system (bunch by bunch, intra-bunch)
 large tune spread (but acceptable level in betatron resonance)
to suppress instabilities: optimizing bunching factor & chromaticity
Some items are relating with multiple sources, especially Tune spread & instability.
Beam loss localization with collimators is needed, also.

## Slide 11: Beam loss sources and Tuning Items for Fast Extraction
Beam loss sources in MR
Upstream beam quality from RCS:
 In Transverse, to choose optimal conditions with 3-50BT OTR monitor
Physical aperture
 to hold effective aperture with closed orbit correction, optics correction
Emittance growth by Betatron resonances
 To choose optimal operation point considering
- Tune spread by space charge
 to control high bunching factor with higher harmonic RF
- Tune spread by chromaticity
 patterned Chromaticity correction with sextupoles
- Resonance strength
 to enlarge dynamic aperture by
leakage field corrections with Trim-quadrupoles
resonance corrections with Skew-quadrupoles, Trim-Sextupoles
optics meas. & correction not only injection period but acceleration period
Emittance growth by beam instability (impedance from resistive wall)
 transverse feedback system (bunch by bunch, intra-bunch)
 large tune spread (but acceptable level in betatron resonance)
to suppress instabilities: optimizing bunching factor & chromaticity
Some items are relating with multiple sources, especially Tune spread & instability.
Beam loss localization with collimators is needed, also.

## Slide 12: Resonance lines and Estimated Tune Spread 380 kW
MR Power 380 kW
MR Cycle: 2.48 s
Number of protons: 2.5e13 ppb
Transverse Emittance: 16π mmmrad
Bunching Factor: 0.3
Space Charge Tune Shift: 0.33
E = 3 GeV
(v/c)2γ3=69.751
2RN = 2.5×1013×9 : Intensity
42/ = 16 mmmrad : Emittance
Bf = 0.3 : Bunching factor
νy=21
2νx−2νy=3
νx−2νy=−19
22.5
νx+2νy=64
νx+νy=43
2νx=45
2νy=41
3νx=67
νx=22
22.0
20.5
21.0

## Slide 13: Longitudinal Profiles with High Intensity Beam of 500 kW equivalent
(100 kV, 0 kV)
Bunching factor
0.2 ~ 0.3
Bunch length
~200 ns
(100 kV, 70 kV)
Bunching factor
0.3 ~ 0.4
Bunch length
~400 ns
Simulation
(100 kV, 0 kV)
Simulation
(100 kV, 70 kV)

## Slide 14: RF Pattern
RF pattern :
  Injection : 160 kV (fundamental), 85 kV (2nd harmonic)
  Acceleration : 280 kV → 256 kV (fundamental)
Beam loading compensation effectively works to reduce longitudinal oscillations.
Bunching factor was measured to be 0.3 during injection.
Longitudinal wave forms
during injection
with wall current monitor
K1
K2
K3
K4

## Slide 15: Chromaticity Pattern for Instability Suppression
The chromaticity pattern was optimized to minimize the beam loss.
To suppress instabilities the chromaticity is kept to be negative, typically −6 during injection.
If the chromaticity is too small in negative value, we observe instability.
If the chromaticity is too large in negative value, we observe beam losses those are probably due to chromatic tune spread.
Instabilities are suppressed with bunch by bunch feedback and intra-bunch feedback system.
The optimization is iterated after the change of parameters feedback systems.
Instability
Chromatic tune spread larger
X
Y
K1
P2
2.53e13 ppb * 8 bunches
40 ms
Single Pass Monitor
Right – Left
Top – Bottom

## Slide 16: Bunch by Bunch and Intra-bunch Feedback
Coherent Oscillation is damped with the bunch by bunch and intra-bunch feedback system during injection and in the beginning of acceleration.
Intra-bunch FB has been applied during injection and up to 0.2 s after acceleration start.
P1+100 ms P2
P1+100 ms P2
Beam Position with Intra-bunch FB off
Beam Position with Intra-bunch FB on
2.1e13 ppb × 2 bunches
Intra-bunch feedback system (wideband)
Bunch by bunch feedback system

## Slide 17: FX Septum Leak Field
Chart: 
| -1.7999999999999999E-2 | -8.9999999999999993E-3 | 0 | 8.9999999999999993E-3 | 1.7999999999999999E-2
 | 0.00065666 | 0.00051275 | 0.00037464 | 0.00023761 | 9.6763e-05
x[m]
BL[Tm]
SM30 (336A) with duct
QFR
154
QDT
155
QFP
156
SM11-22
SM30-33
Trim coils of 3 Q magnets have been used to correct the leak field of FX septum magnets.
FX septum magnets makes undesirable Q fields for circulating beam with the leak fields.
Leak field of 8 FX septum magnets corresponds to ~3% of K1 of the main Q magnet.
βx, βy
dβx, dβy
Optics before Correction at (22.19, 20.54)
Optics after Correction at (22.19, 20.54)
βx, βy
dβx, dβy
βx, βy
dβx, dβy
βx, βy
dβx, dβy
βx, βy
dβx, dβy
βx, βy
dβx, dβy

## Slide 18: 3rd Order Resonance Corrections with Trim Coils of Sextupole Magnets
νx+2νx=64
8e11ppb, 1 bunch injection at k1
3 GeV DC
Search the resonance with worse beam survival around (22.42, 20.78).
Beam survival recovers with SFA048: +1.1 A, SFA055: 0 A.
3νx=67
Search the resonance with worse beam survival around (22.34, 20.75).
Beam survival recovers with SFA048 −0.3 A, SFA055 −0.0 A.
Both resonances of νx+2νy = 64 and 3νx=67 were corrected with SFA048 +0.86 A, 055 −1.15 A, 062 +1.26 A, 069 −0.85 A.

## Slide 19: Operation with the Betatron Tune of (21.35, 21.43)
(21.35, 21.43)
(22.40, 20.75)
Structure resonances of up to 3rd order (Solid lines)
Non-structure resonances of half integer and linear coupling resonances (Dashed lines)

## Slide 20: Optimization for (21.x, 21.x)
νx - νy = 0
νx – 2νy = -21
νy = 21
νx = 21
νx + 2νy = 64
3νx = 64
2νy = 43
Dynamic Aperture Survey Simulation
B,Q,S field errors : ON
Alignment errors : ON
dp/p0 = 0.0%
FX septum leakage : OFF
3rd resonance corr. (Trim-S) : OFF
Emittance : 80π (2π step), Turn : 2000
(21.23,21.30)
(21.36,21.43)
νx + 2νy = 64
3νx = 64
Survival during inj. for 390 kW equiv. beam
νx
νy
2νx = 43
Optics correction
Tune scan
2nd rf operation
Trim Q correction for FX septum mag.
Trim S correction for 3rd order res.
Skew Q correction for νx − νy = 0
Octupole correction
Instability suppression
  Chromaticity: −7
  Bunch by bunch and intra-bunch FB
Extraction orbit for neutrino beamline
Compensation kicker is not optimized yet.

## Slide 21: 440 kW Trial with (21.35, 21.43)
Injection
Acceleration
Extraction
Recovery
2016/5/25 21:28: Trial shots to MR-abort with the betatron tune of (21.35, 21.43)
Power : 440 kW
Repetition : 2.48 sec
4 batch (8 bunch) injection during the period of 0.13 s
2.9e13 protons per bunch (ppb) × 8 @ Injection
2.27e14 ppp @ P3 (end of acceleration)
Loss during the injection period : 443 W
Loss in the beginning of acceleration (0.12 s) : 795 W
Loss power is within the MR collimator limit of 2 kW.
0.01 + 0.13 s
1.4 s
0.94 s
Time (s)
Beam Intensity with DCCT

## Slide 22: 30GeV acceleration in (21.24, 21.31)
Beam oscillation
signal
Horizontal
Vertical
MR intensity : 530kW-eq. (2bunches)
Ion source 40 mA
Tune: (21.24, 21.31)
Structure res. corr. by 3 Trim-Qs
Correction of 3rd resonance lines by 4 Trim-Sexts
Chrom. Corr. 75% DC for reduction of instability
No 2nd harmonic RF
Tunable knobs to be optimized:
Transverse feedback
Patterned resonance correction
2nd harmonic RF cavity
Compensation kickers for injection
(21.24, 21.31)
132kW @ 2bunches injection
0.42 kW beam loss
H-V-60pi collimation at Collimator
Instability beam loss
(22.40, 20.75) w 2nd harmonic RF
Number of bunches | Repetition period (s) | Beam power (kW) | Beam loss (kW) | Notes
2 | 2.48 | 132 | 0.42 | Measurement
8 | 2.48 | 530 | 1.7 | Estimation
8 | 1.3 | 1000 | 3.2 | Estimation
Using 2nd harmonic RFs, we can increase BF ~1.5 times. Ion source 50 mA available.
 1.3 MW operation is in scope under ~full chromatic corr. w/o causing instability.
Notes: Instability but lots of tuning nobs: 520 kW w ~ 2kW loss  1MW in scope w nobs

## Slide 23: Recent keys of FX tunings
2014 summer - 2015 spring (Linac Current Upgrade 30 -> 40~50 mA)
Installation OTR monitor at 3-50BT: choosing best upstream conditions
Installation Transverse intra-bunch feedback: instabilities well suppressed
Optics correction; Optimizing correlation of RF setting, chromaticity correction pattern, and transverse feedback to suppress instability
New Trim-quadrupoles to correct leakage field of FX septum
New Trim-sextupoles to correct 3rd resonance line
2nd harmonic RF 30 kV: bunch length kept avoiding extra kick from injection kickers

## Slide 24: Recent keys of FX tunings
2015 summer - 2016 spring
- Adding angle moving collimators in MR: capacity 2 -> 2.5 kW, beam loss well localized
- Installation of compensation kicker: to compensate extra kick of injection kickers, longer bunch available
- Optics correction during acceleration, Tune tracking
- 2nd harmonic RF 70 - 85 kV, longer pattern: longer bunch and controlled momentum spread
- Operation point shift trial: (22.40, 20.75) -> (21.35, 21.43) to avoid half-integer resonance
- Trim-Q & Trim-S acceleration pattern
- Optimizing Octupoles

## Slide 25: Outline
Introduction
  J-PARC MR and FX operation
Recent tunings
  Beam loss sources
  instability: chromaticity correction and transverse feedback
  optics correction during acceleration
  resonance corrections
  2nd harmonic rf: larger bf, less sc effect
  New operation point explore
Midterm plan
  High repetition scenario
  For > 1MW
Summary

## Slide 26: Mid-term plan of MR FX operation
JFY | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
FX power [kW] | 390 | 425-450 | 450-500 | 700 | 800 | 900 | 1060
Cycle time of main magnet PS New magnet PS | 2.48 s |  |  | 1.3 s | 1.3 s | 1.25 s | 1.20 s
High gradient rf system 2nd harmonic rf system |  |  |  |  |  |  | 
Ring collimators | Add.collimators (2 kW) |  | Add.colli. (3.5kW) |  |  |  | 
Injection system FX system |  |  |  |  |  |  | 
Mass production
installation/test
Manufacture, installation/test
Kicker PS improvement, Septa manufacture /test
Kicker PS improvement, FX septa manufacture /test
Installation
New PS buildings
2.48 s →1.3 s
Faster Cycling 2.48 s → 1.3 s or Faster
Linear increase both beam power & loss
We are going to upgrade
Magnet Power Supply
RF
Injection and Extraction Devices
MR collimator upgrade

## Slide 27: Mid-term plan of MR FX operation
JFY | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
FX power [kW] | 390 | 425-450 | 450-500 | 700 | 800 | 900 | 1060
Cycle time of main magnet PS New magnet PS | 2.48 s |  |  | 1.3 s | 1.3 s | 1.25 s | 1.20 s
High gradient rf system 2nd harmonic rf system |  |  |  |  |  |  | 
Ring collimators | Add.collimators (2 kW) |  | Add.colli. (3.5kW) |  |  |  | 
Injection system FX system |  |  |  |  |  |  | 
Mass production
installation/test
Manufacture, installation/test
Kicker PS improvement, Septa manufacture /test
Kicker PS improvement, FX septa manufacture /test
Installation
New PS buildings
In 2.48 s cycle, MR has been accelerated 2.7e13 ppb (420 kW) in user operation, and 3.4e13 ppb (530 kW equivalent) in demonstration.
Achieving > 750 kW user operation and aiming > 1 MW are reasonable as beam dynamics in 1.2 ~ 1.3 s cycle.
For the faster cycle, we are going to upgrade Magnet Power Supply, RF, Injection and Extraction Devices, MR collimator as follows.

## Slide 28: Summary
Beam power of 420 kW has been achieved for FX user operation with
  Injection beam distribution by RCS tuning
  Rf pattern optimization for fundamental and 2nd harmonic
  Bunch by bunch feedback and intra-bunch feedback
  Optics correction and resonance line corrections
  and so on.
Operation with the betatron tune of (21.35, 21.43) has been started.
  There is more free space without serious resonances.
  This operation area can accelerate 530 kW equivalent beam.
We plan to achieve the target beam power of 750 kW and more with the faster cycling 2.48 s to 1.3 s. We are upgrading the following hardware by JFY 2018.
  Main magnet power supplies
  Rf
  Injection and extraction devices
  Collimators
> 1MW beam operation is good target in our scope.

## Slide 29: References

## Slide 30: Recent keys of FX tunings
2014 summer - 2015 spring (Linac Current Upgrade 30 -> 40~50 mA)
Installation OTR monitor at 3-50BT: choosing best upstream conditions
Installation Transverse intra-bunch feedback: instabilities well suppressed
Optics correction; Optimizing correlation of RF setting, chromaticity correction pattern, and transverse feedback to suppress instability
New Trim-quadrupoles to correct leakage field of FX septum
New Trim-sextupoles to correct 3rd resonance line
2nd harmonic RF 30 kV: bunch length kept avoiding extra kick from injection kickers

## Slide 31: Recent keys of FX tunings
2015 summer - 2016 spring
- Adding angle moving collimators in MR: capacity 2 -> 2.5 kW, beam loss well localized
- Installation of compensation kicker: to compensate extra kick of injection kickers, longer bunch available
- Optics correction during acceleration, Tune tracking
- 2nd harmonic RF 70 - 85 kV, longer pattern: longer bunch and controlled momentum spread
- Operation point shift trial: (22.40, 20.75) -> (21.35, 21.43) to avoid half-integer resonance
- Trim-Q & Trim-S acceleration pattern
- Optimizing Octupoles

## Slide 32: History of MR beam power
Earthquake recovery
Hadron Exp. Facility upgrade
2010 summer - 2011 spring
FX kicker upgrade: 6 -> 8 bunch operation
Additional shields of 3-50BT collimator: capacity 0.45 -> 2 kW
Installation of Transverse bunch by bunch feedback
Cycle: 3.52 -> 3.2 ~ 3.04 s

## Slide 33: History of MR beam power
2011 summer - 2012 spring
Injection kicker upgrade: less extra kick and less impedance
Installation of 7th and 8th RF system
Installation of 4 Skew Qs: correct sum resonance
Installation of 3 Octupoles: beam stability
Cycle: 3.04 -> 2.56 s
Earthquake recovery
Hadron Exp. Facility upgrade

## Slide 34: History of MR beam power
Earthquake recovery
Hadron Exp. Facility upgrade
2012 summer - 2013 spring
Additional shields and absorber of MR collimator: capacity 0.45 -> 2 kW
Installation of 9th RF system
Installation of additional 3 Octupoles: beam stability
Cycle: 2.56 -> 2.48 s

## Slide 35: History of MR beam power
Earthquake recovery
Hadron Exp. Facility upgrade
2013 summer - 2014 spring (Linac Energy Upgrade 181 -> 400 MeV)
Additional shields and collimators of MR collimator: capacity 2 -> 3.5 kW
Replacement of a part of beam ducts: SUS -> Ti reducing residual radiation dose
Improvement of injection kicker system: its rise time shorter

## Slide 36: History of MR beam power
Earthquake recovery
Hadron Exp. Facility upgrade
2014 summer - 2015 spring (Linac Current Upgrade 30 -> 40~50 mA)
MR collimator repair: capacity 3.5 -> 2 kW
OTR monitor at 3-50BT: choosing best upstream conditions
Installation of Transverse intra-bunch feedback
Optics correction; Optimizing correlation of RF setting, chromaticity correction pattern, and transverse feedback to suppress instability
Installation of Trim-Qs to correct leakage field of FX septum
Installation of Trim-Ss to correct 3rd resonance line
2nd harmonic RF 30 kV: bunch length kept avoiding extra kick from injection kickers

## Slide 37: History of MR beam power
Earthquake recovery
Hadron Exp. Facility upgrade
2015 summer - 2016 spring
Adding angle moving collimators in MR: capacity 2 -> 2.5 kW
Installation of compensation kicker: to compensate extra kick of injection kickers
Optics correction during acceleration, Tune tracking
2nd harmonic RF 70 - 85 kV, longer pattern
Operation point shift trial: (22.40, 20.75) -> (21.35, 21.43) to avoid half-integer resonance
Trim-Q & Trim-S acceleration pattern
Optimizing Octupoles
The max. delivered beam power ~ 425 kW (2.2x1014 ppp)

## Slide 38: RCS調整による入射ビーム分布の改善
RCSビームスタディにより、MR大強度運転のためのRCSでの入射ペイントおよびチューン設定等のパラメータの最適化を行っている。
3-50BTの optical transition radiation monitor (OTR) で横方向分布を測定。
ビーム強度 3.48e13 ppb
RCS 830 kW 相当、MR 540 kW 相当。
RCS 50π correlated paint
水平方向エミッタンス (100%) : 26.8π mmmrad
垂直方向エミッタンス (100%) : 24.6π mmmrad
OTRでのβを設計値 βx = 27.2 m, βy = 17.9 m を仮定。
Hori. emit. (full)
26.8π mmmrad
Vert. emit. (full)
24.6 mmmrad

## Slide 39: 入射キッカー波形
バンチ長が長くなり入射キッカーに改善が必要となった。
立ち上がり時間とテールは回路の改良で改善した。
反射波が周回ビームをキックする。
補正キッカーにより余計なキックを戻すようにした。
入射時のビームロスも減少した。
Previous Injection

## Slide 40: Linear Coupling Resonance Correction with Skew Quadrupole Magnets
Measured beam survival
on LCR (22.28, 20.71)
w changing Skew Q
No correction
Corrected with 3 GeV DC
Corrected from 3 to 30 GeV
Skew Q setting reduces beam loss in high intensity operation and is used for the user operation.
Flat Base
Acceleration
1E12ppb
2E11ppb
Beam Intensity
Simulation for tune survey for aperture w/o Skew Q, with Skew Q
Injection
Acceleration
2 bunch injection 380 kW equiv.

## Slide 41: 3rd Order Resonance Corrections with Trim Coils of Sextupole Magnets
νx+2νx=64
8e11ppb, 1 bunch injection at k1
3 GeV DC
Search the resonance with worse beam survival around (22.42, 20.78).
Beam survival recovers with SFA048: +1.1 A, SFA055: 0 A.
3νx=67
Search the resonance with worse beam survival around (22.34, 20.75).
Beam survival recovers with SFA048 −0.3 A, SFA055 −0.0 A.
Both resonances of νx+2νy = 64 and 3νx=67 were corrected with SFA048 +0.86 A, 055 −1.15 A, 062 +1.26 A, 069 −0.85 A.

## Slide 42: Correction of the 3rd Order Resonances of both νx+2νy = 64 and 3νx = 67
069
062
048
069
062
048
055
055
1+2
3+0
Re (G)
Re (G)
Im(G)
Im(G)
Equations for canceling both resonances, for k2(1), k2(2), k2(3), k2(4).
1 = SFA048, 2 = SFA055, 3 = SFA062, 4 = SFA069
k2(j)
k2(j)
k2(j)
k2(j)
k2(1)
k2(1)
k2(1)
k2(1)

## Slide 43: Correction of the 3rd Order Resonances of both νx+2νy = 64 and 3νx = 67 (or 64)
Beam losses were reduced with the correction during injection and the beginning of acceleration for high intensity beam of 380 kW equivalent.
Correction of both νx+2νx=64 and 3νx=67 for tune of (22.40, 20.75)
Correction of both νx+2νx=64 and 3νx=64 for tune of (21.36, 21.43)
Injection
Acceleration
Injection
Acceleration

## Slide 44: Mid-term plan of MR
JFY | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 |  |  |  | HD target (80kW) |  |  | HD target (>100 kW)
FX power [kW] SX power [kW] | 390 42 | 425-450 42-50 | 450-500 50 | 700 50-70 | 800 80 | 900 80 | 1060 ~100
Cycle time of main magnet PS New magnet PS | 2.48 s |  |  | 1.3 s | 1.3 s | 1.25 s | 1.20 s
High gradient rf system 2nd harmonic rf system |  |  |  |  |  |  | 
Ring collimators | Add.collimators (2 kW) |  | Add.colli. (3.5kW) |  |  |  | 
Injection system FX system |  |  |  |  |  |  | 
SX collimator / Local shields |  |  |  |  |  |  | 
Ti ducts and SX devices with Ti chamber |  |  | ESS |  |  |  | 
Mass production
installation/test
Manufacture, installation/test
Kicker PS improvement, Septa manufacture /test
Kicker PS improvement, FX septa manufacture /test
Local shields
Installation
New PS buildings

## Slide 45: Faster Cycling 2.48 s → 1.3 s or Faster
Not allowed by Tokyo Electric Power Company
2.48 s →1.3 s
Issue：Large power variation @ AC main grid
磁気エネルギーの流れ
~D140MW
2.56sec cycle
1.3 sec cycle
Energy Recovery with Bank Capacitor
Requirement to the magnet power supplies
Present
All magnetic energy recover to AC main.
New
All magnetic energy recover to capacitor bank
Magnetic Energy
Magnetic Energy
AC main
AC main
Magnet Power Supply
RF
Injection and Extraction Devices

## Slide 46: RF Cavities
& 2nd Harmonic Cavity in Ins.-A
FT3L (for High Gradient Cavity)
7 × 5-cell cavity + 2 × 4-cell cavity: 602 kV
Required voltage for 1.3 s cycle: 540 kV
FT3M 9 × 3-cell cavity: 315 kV
Required voltage for 2.48 s cycle: 280 kV
INS-C FY2012
Four cavities ⑤〜⑧ will be installed in this summer.
Plan FY2016
①
②
③
④
⑨ in 2013
❺
❻
❼
❽
⑤
⑥
⑦
⑧
Photo of ①〜③ cavities installation in 2015